## Slide 1: MMEdge: Accelerating On-device Multimodal Inference via Pipelined Sensing and Encoding
Runxi Huang, Mingxuan Yu, Mingyu Tsoi, Xiaomin Ouyang
Department of Computer Science and Engineering
Hong Kong University of Science and Technology
ACM/IEEE SenSys 2026

## Slide 2: Multimodal Sensing Systems
Applications
Autononous Driving
Unmanned Aerial Vehicle
Mobile GUI Agent
Real-time requirements
Privacy concern and network fluctuation
On-device multimodal system

## Slide 3: Multimodal Sensing Systems
Sensing
Radar
Camera
Unimodal Encoding
Video Encoder
Radar Encoder
Multimodal Fusion & Prediction
Prediction: Bounding Box
Traditional sequential processing framework incurs large latency:
blocking unimodal encoding until all data arrives
On-device multimodal inference system

## Slide 4: Our key idea is to pipeline sensing and encoding into smaller units
Unimodal Encoding
Sensing
Radar
Camera
Radar Encoder
Video Encoder
Hide model inference during sensing interval

## Slide 5: MMEdge: System Overview
The first pipelined sensing and encoding framework for on-device multimodal system
RGB
Encoder
Radar
Encoder
Adaptive Multimodal Configuration
RGB
Encoder
RGB
Encoder
Radar
Encoder
Radar
Encoder
Multimodal
Streaming Data
Camera
Radar
Sensing Interval: 50ms
Encoding Latency: 40 ms
Encoding Latency: 60ms
(ResNet-18 -> ResNet-50)
Sensing Interval 70ms
Alternating-based Temporal Aggregation

## Slide 6: Evaluation: Experiment Setting
Multimodal applications across 5 different modalities
7 SOTA Baselines
  Blocking Inference
  Non-blocking Inference
  Modality Gating (RTSS’23)
  Modality Imputation (MobiSys’21)
  Model Selection
  Pipeline Min
  Pipeline Max
NVIDIA Jetson Xavier NX 16GB
System implementation on edge devices
UAV Testbed
Task | Dataset | Modalities | Models | # Samples
Audio-Visual Speech Recognition | LRW |  | ResNet CNN | 50000
Autonomous Driving VQA | NuScenes-QA-Mini |  | ResNet, OPT-125M LLM | 4458
Real-time Human Tracking | Self-collected UAV |  | YOLO, ResNet | 5687

## Slide 7: Evaluation: Real-world UAV Case Study

## Slide 8: Evaluation: Overall Performance
Performance on Different Tasks
  MMEdge achieves the best trade-off between latency and accuracy
Speech Recognition
Autonoumous Driving QA
UAV-based Human Tracking

## Slide 9: Understanding Performance of MMEdge
Effectiveness of pipelined framework
Effietiveness of adaptive multimodal configuration
Q3 (“existence detection”) configuration: 6FPS, Resnet-18
Q0 (“vehicle count”) configuration: 12FPS, Resnet-50

## Slide 10: Conclusion
MMEdge: the first on-device pipelined sensing and inference framework
  Alternating-based temporal aggregation
  Adaptive multimodal configuration optimizer
Online profiling for rapid runtime dynamics
Generalization of learning-based modules
New applications
Future Work:

## Slide 11: Thanks!
  Full Paper: MMEdge: Accelerating On-device Multimodal Inference via Pipelined Sensing and Encoding (Accepted by SenSys’26)
Github Code
HKUST MINSys Lab
Demo Video
  MMEdge: Accelerating on-device Multimodal Inference via Pipelined Sensing and Encoding
  Runxi Huang, Mingxuan Yu, Mingyu Tsoi, Xiaomin Ouyang

## Slide 12: Appendix: Efficient Temporal Aggregation
Alternating temporal shift
Extracting temporal difference feature

## Slide 13: Appendix: Adaptive Multimodal Configuration
Motivation: Dynamic configuration selection under latency constraint with different decoding latency
  Offline Stage
    Training accuracy predictor
    Profiling decoding latency
  Online Stage
    Data input + Resource availability
Design of multimodal configuration optimizer

## Slide 14: Appendix: Cross-modal Speculative Skipping
Train a light-weight gating classifier
Prediction with partial data from slower modality and full data from faster modality
Skip when prediction is confident

## Slide 15: Appendix: Overhead Evaluation
All designed module with little overhead